## Slide 1: Improving Privacy in Communication Aids
Jack Browne, Mcomp – Jack@e-g-c.co.uk
Dr. Peter O’Neill, PHD – P.O’Neill@shu.ac.uk

## Slide 2: About the authors
Jack Browne
  Occupation: Computer and Information Security at Kilco IT
  Masters in Computer and Information Security at Sheffield Hallam University
  Specific Focus: User security & seamless security
Dr. Peter O’Neill
  Occupation: Senior Lecturer at Sheffield Hallam University
  PhD Title: "Enhancing the Prescription of Electronic Assistive Technology"
  Previous Employment: Barnsley Hospital NHS Foundation Trust and the University of Sheffield, Madhouse Software Production Ltd

## Slide 3: Background to the research
Masters level group project
  Combined multiple disciplines
  Applied the skills to an unknown environment
  Goal: Produce a VOCA for a specific disability profile
Discipline specific research
  Investigate what work has been done
  Identify any gaps in current research
  Try to improve VOCAs by utilising your own skillset

## Slide 4: Initial thoughts
Highly sceptical
  Inverse relationship between usability and security
Communication aids must focus on usability
  Average conversation 120-180 words/minute (Hawking 2004)
  Average typist 40-60 words/minute
  Communication aids are significantly lower
However
  Little or no research into communication aid security
  Opportunity to improve security with minimal usability impact

## Slide 5: Information Security Triad
Confidentiality
  “Protecting the information from disclosure to unauthorised parties”
Integrity
  “Maintaining the consistency, accuracy, and trustworthiness of data over its entire life cycle”
Availability
  “Providing a certain measure of redundancy and failover”

## Slide 6: The Triad in VOCAs
Integrity
  Very small chance of input or output being tampered with
  Short data lifecycle
Availability
  Extended batteries
  Redundant power supply
  Reliable operating systems
Confidentiality
  Information input is unprotected
  Information output is unprotected

## Slide 7: Insecure Input of Information
Input screens publicly viewable
  Designed around usability
  Maximum visibility
What if…
  User wants to communicate private information
    Address/phone details
    Bank details
    Medical information
Anyone within view of the screen can read it!

## Slide 8: Insecure Output of Information
Many VOCAs use a speaker
  Anyone in the room can hear the speaker
  Only supports 1-to-many communication
What if…
  User wants to communicate private information
    Address/phone details
    Bank details
    Medical information
Anyone in the room can hear it!

## Slide 9: Aims
To improve privacy/confidentiality in communication aids
  Securing the input of information
  Securing the output of information
Minimise impact on usability of communication aids – irrelevant of disability

## Slide 10: Input of Information - Solutions
Common problem in many areas
  Mobile computing
  Public kiosks
  ATMs
Solution: Physical Privacy Filters
  Applied over the screen as a film
  Only allow viewing from a perpendicular angle
  Side, top & bottom view obscured

## Slide 11: Physical Privacy Filters
Advantages
  Cheap to produce
  Easy to use
  Adaptable to many devices
  Can be retro-fitted
Disadvantages
  Filters sometimes fall off
  What if the screen angle is knocked and user has physical disability?

## Slide 12: Software Based Privacy Filters
Laptop with privacy mode – Dell (2008)
  Turned on/off instantly
  Cost ~£83.50
  Small in comparison to cost of advanced communication aids

## Slide 13: Software Based Privacy Filters
Advantages
  Can be enabled/disabled at the touch of a button
  Can be used with minimal effort
  Relatively cheap to implement
Disadvantages
  Requires installation of additional privacy button
  Can’t be retro-fitted to devices
Overall appeared to be a robust and adaptable solution

## Slide 14: So far…
Software based privacy filter
  Secures the input of data to devices
  Doesn’t secure the output of data
Users should be able to communicate information discretely
  Support 1-to-1 communication
Not all communication is suitable for 1-to-many output

## Slide 15: Just Talk V1.0
Madhouse Software
  Supported multiple selection layers
  Originally used to convey emotion
Allows for volume selection on output
  0.5 second hold  Layer 1  Whisper
  1.0 second hold  Layer 2  Speak
  1.5 second hold  Layer 3  Shout
Layers can be prioritised based on frequency
Improvement:
  Allow ‘whisper’ option to be routed to headphones

## Slide 16: Routing Audio to Headphones
Problem
  What if communication recipient is unable to pick up headphones?
  What if communication recipient is deaf?
Solution
  Install an additional output screen
  Toby Churchill Lightwriter SL40
Whispering = Screen + Headphones
Speaking/Shouting = Screen + Speaker
Apply digital privacy filter to both input and output screens

## Slide 17: Combination of solutions
A communication aid which…
  Allows information to be input privately
  Supports discrete 1-to-1 communication
  Supports disabilities in both users and conversation recipients
  Minimal impact on usability
  Minimal increase in cost
Lessons learned are more important…

## Slide 18: Lessons Learned
Usability improvements are a priority
  Aim for conversational speech
  Increase independence of users
  Range of use increases
Result: A need for devices which support discrete communication
  Minimal demand at the moment
  It’s ok to be ahead of the curve
  We don’t need to re-invent the wheel
Important not to get tunnel vision
  Communication involves more than words per minute
  Direction, emotion, independence

## Slide 19: Thank you
Any questions?